## Slide 1: Software-Based Medical Devices
Harold Wodlinger
April 30, 2007

## Slide 2: Abstract
  An overview of software-based medical devices and the regulations and standards that they meet.
  Some examples to be covered include Surgical Navigation systems, implantable pacemaker/defibrillators, computer-aided diagnostics, and PACS/EMR systems.
  Regulations and standards covered include FDA, HIPAA, DICOM, HL7 and IHE.

## Slide 3: A Case Study in the Modern Digital Hospital

## Slide 4: Case Study
Patient presents at ER complaining of chest pain
Waits 6 hours (Canadian model)
Entered in ADT system, Physician orders ECG and cardiac enzymes

## Slide 5
I

## Slide 6: ECG Software
Signals converted to digital, with digital filtering and noise suppression
Auto-interpretation – intervals, amplitudes and suggested diagnosis – these programs now match the interpretation skills of the best Cardiologists
ECG Management systems – test is sent automatically to the management system and is then available on any workstation and becomes part of Electronic Medical Record

## Slide 7: Positive ECG: Patient given Cardiac CT (US model)

## Slide 8: CT Software
UI and control of scanner
Mathematical reconstruction of slices
3D presentation, including automatic segmentation of heart and coronary arteries, curved segmentation of the coronary arteries and measurement of stenosis
Archive to PACS system for reading and interpretation at remote workstation, inclusion in EMR

## Slide 9: Positive Cardiac CT – Patient sent to the Cath Lab for stenting

## Slide 10: Results:

## Slide 11: Cath Lab Software
Cath Lab recording system including intracardiac pressures and ECG, conscious-sedation monitoring, angio import and automated QCA (quantitative coronary angiography):

## Slide 12: More Cath Lab Software
Report generation and distribution to Cardiologist
Inventory update and automatic ordering of devices used
Automated reporting to ACC nationwide registry
Automated billing
Archiving of all images, waveforms, vitals and reports to Cardiac PACS
All data included in EMR

## Slide 13: Selected Cool Software Applications

## Slide 14: Surgical Navigation
Fiducials attached to Patients head
Pre-op CT
Tracking of all surgical instruments in free space in 6D (3D plus yaw, roll and pitch) using optical or magnetic systems
Instruments are registered to CT by touching fiducials
Distal tips of instruments are tracked within the CT image, allowing Surgeons to operate without direct visualization
Surgical Navigation allows much more aggressive surgery

## Slide 16: Implantable Pacemaker/Defibrillators
Antitachycardia pacing
Defibrillation
Dual chamber rate responsive pacing therapy
30 J within 7 seconds charge time
79 grams
40 cc
6.1 years

## Slide 17
ICD Software
Algorithm to distinguish
Atrial Tachycardia from
VT/VF

## Slide 18: Computer-Aided Diagnosis Breast Cancer

## Slide 19: Computer-Aided Diagnosis Breast Cancer
More than eight million women a year have their mammograms interpreted with the aid of CAD
Independent prospective studies from clinical sites have shown an 8-19% increase in cancer detection from academic and community practices, respectively

## Slide 20: Computer-Aided Diagnosis Colon Cancer

## Slide 21: 3-D Virtual Colonoscopy: A Breakthrough for Colon Cancer Screening
Sensitivity of Virtual colonoscopy vs. conventional colonoscopy:
93.8% and 87.5%, respectively, for detecting polyps of 10 mm or larger in diameter
93.9% and 91.5% for polyps of 8 mm or larger
88.7% and 92.3% for polyps of 6 mm or larger.

## Slide 22: PACS/EMR
PACS completely replaces film in hospitals - any image, any time, any place
EMR completely replaces paper
Benefits:
  Patient files available, accessible, complete, and include both data and reports
  Outcomes analysis by department, hospital, country
  Web-based data access
  Highly efficient work flow
  Reduction in medical and prescription errors
The PACS market - $4.9 Billion in 2006, CAGR of 12%, to $8.6 billion in 2011.

## Slide 23
Our Mission:
To foster and accelerate the development and adoption of electronic health information systems with compatible standards and communications technologies on a pan-Canadian basis, with tangible benefits to Canadians.
Our Vision
A high-quality, sustainable and effective Canadian healthcare system supported by an infostructure that provides residents of Canada and their healthcare providers with timely, appropriate and secure access to the right information when and where they enter into the healthcare system. Respect for privacy is fundamental to this vision.
Our Goal
To have an interoperable EHR in place across 50 per cent of Canada (by population) by the end of 2009.

## Slide 24: Regulations and Standards

## Slide 25: Regulations and Standards
Regulations (mandatory):
  Safety and efficacy: FDA, CE
  Privacy: HIPAA
Standards (optional):
  Compatibility: HL7, DICOM, IHE, SNOMRD, CCOW, ....

## Slide 26
  Medical device amendments of 1976 to the Food, Drug and Cosmetic Act:
    Class 1, General Controls: include premarket notification, good manufacturing practices, truth in labeling, and adequate directions for use.
    Class 2, Special Controls: special rules for particular devices to assure safety and effectiveness of those devices. The general controls also apply.
    Class 3, Premarket Approval: meaning an application (PMA) to market the device would be submitted to the FDA. General controls also apply, and special controls might also apply.

## Slide 27: FDA Requirements
Premarket approval
Design controls, including FMEA, V&V
Compliance with all applicable standards
Proper labeling, including manuals, product labeling, indications and contraindications, marketing materials
Manufacturing controls, including quality system
Post-market surveillance and reporting

## Slide 28: General Principles of Software Validation Final Guidance for Industry and FDA Staff (Document issued on: January 11, 2002)
This guidance applies to:
  Software used as a component, part, or accessory of a medical device;
  Software that is itself a medical device;
  Software used in the production of a device (e.g., programmable logic controllers in manufacturing equipment); and
  Software used in implementation of the device manufacturer's quality system (e.g., software that records and maintains the device history record).

## Slide 30: The Health Insurance Portability Accountability Act (HIPAA): Medical Privacy in the Electronic Age
Enacted in 1996
United States Department of Health and Human Services developed standards and requirements that were published in April, 2001and became fully enforced in April, 2006
Any medical information created, maintained or transmitted electronically must remain secure at all points in the health care delivery chain.

## Slide 31: HIPAA Requirements
All medical records, medical billing, and patient accounts must meet certain consistent standards with regard to documentation, handling and privacy.
All patients must be able to access their own medical records, correct errors or omissions, and be informed who has accessed their information for up to six years prior.
Patients must be notified of privacy procedures
HIPAA requires audit trails of everyone who accessed patient information.

## Slide 32: What does HIPAA require of Software Developers?
Biometric and password access to any system that can display confidential information
Encryption of information sent over networks, email, etc.
Removal of patient names and numbers from screens and documents that can be viewed by the public
Audit systems for access to information

## Slide 33
Hospitals own equipment from multiple suppliers...
They all have to communicate images to the PACS, EMR, referring physician
Before DICOM, every system had a proprietary file structure
DICOM has revolutionized health care software

## Slide 34: DICOM
DICOM, first published in 1993, ensures the interoperability of systems used to:
    Produce, Store, Display, Process, Send, Retrieve, Query or Print
Over 750 technical and medical experts participate in more than 20 active DICOM working groups.
Applied originally to medical images; now includes waveforms, derived structured documents (worklists and reports), and the management of related workflow

## Slide 35
Integrating the Healthcare Enterprise
Similar goals to DICOM and HL7, but focused on Enterprise-wide connectivity
More than 100 vendors have implemented and tested products based on IHE
Process:
I. Identify Interoperability Problems - Clinicians and IT experts II. Specify Integration Profiles. Experienced healthcare IT professionals identify relevant standards and define how to apply them to address the problems. III. Test Systems at the Connectathon. Vendors implement IHE integration profiles in their products and test their systems for interoperability at the annual IHE Connectathon. IV. Publish Integration Statements for use in RFPs.

## Slide 37: IHE Example Stress Echo Image Display
Stress echo images create a unique problem because the order of the display (by view and by stage) is critical
IHE Cardiology requirements:
  specific display requirements based on baseline, pre-, mid-, post-stress, and recovery stages.
  Views, such as Parasternal short axis,
  Protocols, such as Modified Bruce Treadmill
The images are consistently displayed on any IHE compatible workstation, relieving the sonographer or cardiologist of spending time rearranging image sets.

## Slide 38: Thank you